M4:	Skalär ODE:

left lbrace stack{alignl{dot u (t) + Au(t) = F(t), ~~ t > 0} # alignl{u(0) = u^0}} right none

A konstant, F(t) given funktion

Trapetsmetod:

Hitta en styckvis linjär U(t)

U^{n+1} + k over 2 left ( AU^{n+1} + AU^n right ) = U^n + {size *1.25 int from I_{size *1.25 n} ""} F(t)`dt, ~~ n = 1,`2,`...

U0 ≈ u0

Inte en interpolation, men ett försöl att approximera den.

Residual:

R(U) = dot U + AU - F	( R(u) = 0 )

Dualproblem:

left lbrace stack{alignl{-φ + Aφ = 0, ~~ T > t >= 0} #alignl{φ(T) = sgn(e(t))}} right none	Fel: e = u − U

Kommentar:

langle Av;` w rangle = ... = langle v;` "A*"`w rangle	där * är en dualoperator

A = dot v - ∆u

langle dot v + Av;`w rangle = {size *1.25 int ""}v(-dot w + Aw)`dx`dt = langle v;`-dot w + Aw rangle

Felrepresentation:

abs{e(T)} = -{size *1.25 int from 0 to T ""} R(U) φ`dt + e(0)φ(0)	(1)

Låt φ̅, medelvärdet över In:	bar φ(t) = 1 over k {size *1.25 int from I_{size *1.25 n} ""} φ(s) `ds

(φ̅ konstant över In)

Vi har att {size *1.25 int from I_{size *1.25 n} ""} R(U)`dt = 0
⇓
{size *1.25 int from I_{size *1.25 n} ""} R(U) bar φ `dt = 0 ~drarrow~ {size *1.25 int from 0 to T ""} R(U) bar φ `dt = 0	(2)

(1) − (2):

abs{e(T)} ~=~ -{size *1.25 int from 0 to T ""} R(U)(φ - bar φ)`dt ~+~ e(0)φ(0)

⇓

abs{e(T)} ~<=~ sum from {n = 0} to {N - 1} R_n {size *1.25 int from I_{size *1.25 n} ""} abs{φ - bar φ}`dt ~+~ abs{e(0)} cdot abs{φ(0)}

R_n (U) ~≜~ max csub {size *1.25 {t ∈ I_{size *1.25 n}}} ``abs{`R(U(t))`}

A posterion-feluppskattning:

abs{``u(T) - U(T)``} ~ <= ~ S_c (t) `{max csub n}` kR_n(U) ~+~ S_d (t) `abs{`u(0) - U(0)`}

left lbrace stack{alignl{S_d (T) = abs {φ(0)}} # alignl{S_c (T) = {size *1.25 int from 0 to T ""} abs{dot φ}`dt}} right none

Bevis:

{size *1.25 int from I_{size *1.25 n} ""} abs{φ - bar φ}`dt ~<=~ k{size *1.25 int from I_{size *1.25 n} ""}abs{dot φ}`dt	(3)

{size *1.25 int from I_{size *1.25 n} ""} abs{φ - bar φ}`dt~?

φ(t) - bar φ{t} ~=~ 1 over k {size *1.25 int from I_{size *1.25 n} ""} left ( φ(t) - φ(s) right ) `ds	(*)

abs{`φ(t) - φ(s)`} ~=~ abs{{size *1.25 int from s to t ""} dot φ(σ)`dσ} ~>=~ {size *1.25 int from s to t ""} abs{dot φ(σ)`dσ}	(**)

nk ≤ t < s ≤ (n+1)k

{size *1.25 int from I_{size *1.25 n} ""} abs{φ - bar φ} `dt ~ = csub "(*)" ~ {size *1.25 int from I_{size *1.25 n} ""} abs{1 over k {size *1.25 int from I_{size *1.25 n} ""} left ( φ(t) - φ(s) right ) `ds} `dt ~ <= ""

"" <= ~ {size *1.25 int from I_{size *1.25 n} ""} 1 over k {size *1.25 int from I_{size *1.25 n} ""} abs{`φ(t) - φ(s)`} `ds `dt ~<= csub "(**)"~ {size *1.25 int from I_{size *1.25 n} ""} 1 over k {size *1.25 int from I_{size *1.25 n} ""} {size *1.25 int from I_{size *1.25 n} ""} abs{dot φ (σ)} `dσ `ds `dt ~ = ""

"" =~ k {size *1.25 int from I_{size *1.25 n} ""} abs{dot φ (σ)} `dσ	∎

Dual:

left lbrace stack{alignl{- dot φ + Aφ = 0} # alignl{φ(T) = sgn left ( e(t) right ) = +-1}} right none

Exakt lösning:

φ(t) = +- exp left ( -A(T - t) right )

(Primal):

"(P)" `left lbrace `stack{alignl{dot u + Au = F(t)} # alignl{u(0) + u^0}} right none

Stabilitet hos (P) beror på A.

1)	A < 0:	S_d (T) <= exp left (` abs{A}`T `right ),

S_c (T) <= exp(`abs{A}`T`)

2)	A ≥ 0:	S_d(T) <= 1, ~ S_c(T) <= 1

Sc — beräkningsdel
Sd — datafel

Generalisering

1.
left lbrace stack{dot widevec u (t) + {bold A} widevec u (t) = widevec F (t), ~~ t > 0 # alignl{widevec u (0) = {widevec u}^0}} right none ,	widevec u (t) = left ( stack{u_1(t) # u_2(t) # dotsvert # u_m(t)} right ) ,	widevec F (t) = left ( stack{F_1(t) # F_2(t) # dotsvert # F_m(t)} right )
A — m×m-matris
(Modul 4 och 5)

2.	Partiella differentialekationer (PDE):

Hitta widevec u (x;`t):

left lbrace stack{dot widevec u (x;`t) + {bold A} widevec u (x;`t) = widevec F (x;`t) # alignl{widevec u (x;`0) = {widevec u}^0 (x)} # alignl{"randvillkor"}} right none

(Modul 6)

{bold A} widevec u = ∆ widevec u

{bold A} widevec u = β cdot ∇ widevec u - ε∆ widevec u
Dual problem:

left lbrace alignl matrix{"ODE-system:" ~ # - dot φ ``+`` A^T cdot φ ``=`` 0 ## "PDE:" ~ # - dot φ ``+`` "A*" cdot φ ``=`` 0} right none

Exempel:	Mass-fjäder-system:

Koordinater:	x1 (M1)
x2 (M2)

Hastigheter:	v1 (M1)
v2 (M2)

Kraft på M1 från M2:

F_{1,2} ~=~ left lbrace stack{r_{1,2} = abs{x^1 - x^2} # e_{1,2} = {x^2 - x^1} over {r_{1,2}}} right rbrace ~=~ E left ( r_{1,2} - L_{1,2} right ) e_{1,2}

M2 från M1:

F2,1 = −F1,2	(Newtons 3:e lag)

Rörelseekvationer:

left lbrace ~ stack{{dot x}^1 = v^1 # {dot v}^1 = {F_{1,2}} over {M_1}} ~ mline ~ stack{{dot x}^2 = v^2 # {dot v}^2 = {F_{2,1}} over {M_2}} right none

På varje massa Mi, i ≠ 1, m
agerar 2 fjäderkrafter:

left lbrace alignl{stack{F_{i,i-1} ``=`` E left ( r_{i,i-1} - L_{i,i-1} right ) e_{i,i-1} # F_{i,i+1} ``=`` E left ( r_{i,i+1} - L_{i,i+1} right ) e_{i,i+1} }} right none

Rörelseekvation för Mi:

{dot x}^i ``=`` v^i
{dot v}^i ``=`` {~~{{E left ( r_{i,i-1} - L_{i,i-1} right ) e_{i,i-1}} overbrace{size *1.25 F_{size *1.25 {i,i-1}}}}~~} over {M_i} ``+`` {~~{{E left ( r_{i,i+1} - L_{i,i+1} right ) e_{i,i+1}} overbrace {size *1.25 F_{size *1.25 {i,i+1}}}}~~} over {M_i}

Antag E= 1, Mi = 1, Li,j = 0

⇘

{dot v}^i ``=`` {1 cdot r_{i,i-1} ` e_{i,i-1}} over 1 ``+`` {1 cdot r_{i,i+1} ` e_{i,i+1}} over 1

e_{i,j} ``=`` {x_j - x_i} over {r_{i, j}} ``~drarrow~`` {dot v}^i ``=`` left ( x^{i-1} - x^i right ) ``+`` left ( x^{i+1} - x^i right ) ``=`` x^{x-1} - 2x^i + x^{x+1}

dot {widevec u} ~=~ ~ stack{x^1 # x^2 # dotsvert # x^m} over stack{v^1 # v^2 # dotsvert # v^m} ~ ~=~ ~ stack{v^1 # v^2 # dotsvert # v^m} over stack{-x^1 + x^2 # x^1 - 2x^2 + x^3 # dotsvert # x^{m - 1} - x^n} ~ ~=~ ~ left none matrix{ "" # "" # "" # "" ## "" # "" # "" # "" ## "" # "" # "" # "" ## "" # "" # "" # "" ## -1 ~ 1 # "" # "" # "" ## "" # -12 ~ -1 # "" # "" ## "" # "" # -12 ~ -1 # "" ## "" # "" # "" # dotsdown } ~mline~ matrix{ 1 # "" # "" # "" ## "" # 1 # "" # "" ## "" # "" # dotsdown # "" ## "" # "" # "" # 1 ## "" # "" # "" # "" ## "" # "" # "" # "" ## "" # "" # "" # "" ## "" # "" # "" # ""} ~ right none `` ~ stack{x^1 # x^2 # dotsvert # x^m} over stack{v^1 # v^2 # dotsvert # v^m} ~
0
0
0
0
0
0

(Detta är skumt, men vi kommer gå i på det senare.)